SYSTEM

1 > STDOUT
2 > STDERR

NETWORKING

netplan(5) → /etc/netplan

From FHS: (https://refspecs.linuxfoundation.org/FHS_3.0/fhs/ch04s09.html)
   /usr/local
Used as a local software installation directory. Locally
      installed software must be placed in the /usr/local rather
 than /usr unless is being installed to replace or upgrage
software in /usr.

 Local software should not be overwritten when system software
is updated.

[!] therefore it is subdirectories division due to content:
./bin, ./lib.

(https://refspecs.linuxfoundation.org/FHS_3.0/fhs/ch04s11.html)
   /usr/share
Used for all read-only architecture independent data files.

   autoconf	# “configure.ac” => configure
   automake –add-missing	# Makefile.am → from Makefile.in
   ./configure	# generate Makefile from Makefile.in
   make	# build
   make install	# install

  ~darya

/etc/ssh/sshd_config

<Ctrl-R>	reverse search

If package is missing?

apt list <shell_pattern> in the package name

sudo apt search	search in package description

Just find out how prefix is defined.

https://github.com/tmux/tmux

VIM

<Ctrl-W>+<W>	jump to the next split

:only
:set hls	highlight search
:set is ?	Display option status
:set is !	Toggle it’s status ; true → false; false → :true
:set nois
:set nonumber
:split
:close
:source $MY..

:h{elp} ‘is’	option help
:h d	escape mode help

~/.vimrc

$MYVIMRC

SHELL

Shell types:

 Interactive shells:

   /bin/login → /etc/passwd

Who am I?

1. whoami
2. $USER

Environment variables:

To list environments:

 $ env

To set variable:

 $ <variable>=<value>

To export to the current environment:

 $

Shortcuts:

<CTRL>-<u>	delete from cursor to the beginning of the line
<CTRL>-<k>	delete from cursor to the end of the line
<CTRL>-<y>	paste what was deleted by last delete command

<ALT>-<f>	jump word forward
<ALT>-<b>	jump word backwards

<ALT>-<d>	delete till end of the word
<CTRL>-<w>	delete till the beginning of the word

TMUX

 tmux new-session -s <session_name> -c
 tmux kill-session [-t <session_name>] # last session by default
 tmux attach [-t <session_name>]
 tmux ls

 <Ctrl-B> → COMMAND_PREFIX

  “	split window horizontaly
  %	split window verticaly

  o	select next pane
  q	display index on panes; then select them by pressing
on corresponding number key
  <space>	toggle between different pane structures
  w	display windows list
  s	display sessions list
  d	detach
  c	create new window
  n	next window
  p	previous window
  l	last window
  [0-9]	select window by index
  ,	rename pane
  x	close current pane

Accessing command line arguments

ARRAY

CMD[0]

$0 $1 $2
$@

AWK

awk -F[DELIMITER] “/ADDRESS/ {ACTION}”

awk -F: ‘/^fish/ {print $1 “\t” $6}’ /etc/passwd

cut -f[FIELD] -d [DELIMETER]	# default “\t”

DELIMITER = WHITESPACE

Processes

readlink $( ps aux | awk '{ if( $2==1 ) print $11 }' )

ip -o a | awk '/^4/ { if ($3 != "inet6" ) print $4 }'

 systemd

systemctl list-units

to see example service and then
systemctl status <service> | grep Loaded

to see where services are living

/lib/systemd/system most likely

systemctl list-unit-files <service> to see if it’s enabled or not? → list of all unit files
systemctl list-unit-files <service> - list of all unit files of a	specific <service>

apt list “PACKAGE*”
apt show “PACKAGE”
apt install
apt remove

apt list --installed <package> = check if <package> is installed

SSH

[!] Dasha

SHELL

 To get help on any bash built-in command use:
help <built-in>

 Loops:

       / заменено
  FOR <variable> [ [ IN [ WORD ... ] ] ; ] DO LIST; DONE
  \ обязательно \ не обязательно

  FOR <variable> DO LIST; DONE
  FOR <variable> ; DO LIST; DONE
  FOR <variable> IN ; DO LIST; DONE
  FOR <variable> IN <WORD>; DO echo $variable; DO

  Before command is executed all the expansions are processed:

  $(command) or `command` will be substituted by command output
  and further processing will continue

  for variable in list
  do action
  done

  for((i=0; $i -lt 10; ((i++))

  for(i=0; i<10; i++)
action

  ls [OPTION]... [FILE]...

  ls

 File Descriptors:

1	STDOUT
2	STDERR

Login (Interactive)
   /etc/profile (/etc/bash.bashrc /etc/profile.d)
  ~/.bash_profile ~/.bash_login ~/.profile

$$	process name ${$}

PS1

https://ss64.com/bash/syntax-prompt.html

s/pattern/string/[flag]

 Flags:
g	global

VIM

COMMAND MODE	default mode
INSERT MODE	i
VISUAL MODE	v

 H J K L
left down up left

Command mode commands are without prefix (just a key press):

 w
 0	jump to the start of the line
 ^	jump to the first printable character
 N$
 i enter INSERT mode before current character
 I	enter INSERT mode before current character
 a	enter to the INSERT after character
 A	enter INSERT mode at the end of the line

Command line commands are starting from “:”

 :

:help pattern

:[range]co[py] {address}
:{line}

0 zero line (will jump to the line number 1)
$	last line in the file
.	current line
gg	jump to the first line
G	jump to the last line

Range:
 :Start
 :Start,End
 :. default

[count]>>
shift [count] lines one ‘shiftwidth’ rightwards
8 spaces

OPTIONS

All the options has a default value.

To get a value of the current option
   :set <option> ?

 ‘ruler’

‘option’ if in single quotes

:echo &nu
:let &nu=1

vimtutor

Scripting, getting started! Whooohoo!

SCRIPTING

Text processing and manipulation

grep -i ‘^if’
grep -w	# ‘\<word\>’ word boundarys
cut -f1 -d “ “	# dasha, write description!

Shell globs:

* zero or more characters
? one character

Regular expressions:

Character definition

aAbC...	literal meaning
   [a-zA-Z_]	word character	\w
[ \t\n]	not word character	\W
   [0-9] ‘0123456789’	digit	\d
   [a-zA-Z_ \t\n]	not a digit character	\D

Anchors
   ^	beginning of the line
   $	end of the line
   \<	character is at the word boundary
   \>	character is at the word boundary

Character specification:

  CHAR	literally
  . any character

  [[:number:]]

  […]	range

Character repetition:

  CHAR*	character repeats zero or more times
  CHAR\+	character repeats one or more times
  CHAR\?	Character repeats zero or one times

:s/\d\{3,4\}/|\0|/

[0-9a-ZA-Z_]

.* xxx gz.xxx zxx.gz

QUOTES!!!

‘’	no expansion happens
“”	expands varialbe

For example:

seq 0 10 will produce output with the lines
echo $( seq 0 10 )	will substitute new lines by spaces

TO get help on the bash buil-in commands:

help <command>

Utilities for parsing:

tr